## Slide 1
SMART CLASSROOM
AI-Powered Engagement &
Attention Tracking System
Computer Vision • Deep Learning • IoT • Full-Stack Engineering
Final Year Project | Department of Computer Science and Engineering

## Slide 2
THE PROBLEM
Engagement is invisible at classroom scale
01
No objective signal
Instructors rely on a visual scan of the room — subjective, unrecorded, and impossible to scale past ~20-30 students.
02
No early warning
Disengagement (drowsiness, distraction) is noticed only after it has already cost learning time.
03
No longitudinal data
Nothing is logged, so patterns across a semester — or across a whole class — are invisible.
02
SMART CLASSROOM

## Slide 3
OBJECTIVES
What the system sets out to do
1
Real-time multi-face detection & landmark tracking on a standard webcam
2
A configurable weighted attention-scoring engine — not hardcoded thresholds
3
Automated attendance via face recognition
4
Cloud-persisted analytics (Firestore) for longitudinal insight
5
A live dashboard for instructors, plus optional IoT hardware alerts
03
SMART CLASSROOM

## Slide 4
SYSTEM ARCHITECTURE
Layered, dependency-injected pipeline
Client
React Dashboard
Webcam Capture
API
Flask REST API
Classroom Pipeline
CV Modules
Face Detect/Recognize
Eye Track • Head Pose
Sleep/Yawn • Attention
Persistence
Firestore
Attendance • Alerts
Hardware
ESP32
LED • Buzzer • LCD
›
›
›
›
04
SMART CLASSROOM

## Slide 5
THE CORE ALGORITHM
A weighted, configurable attention score
Seven signals, one score (0-100)
Eye Aspect Ratio
20%
Head Pose
20%
Face Presence
15%
Sleep Duration
15%
Blink Rate
10%
Yawn Count
10%
Emotion
10%
Formula
A = Σ wi · Si , subject to Σ wi = 1
Each raw signal Si is normalized to 0-100 by a piecewise-linear function against configured thresholds, then combined by weight and smoothed across frames by exponential moving average — preventing single-frame jitter from swinging the score.
All weights & thresholds live in attention_weights.json — retune without touching code.
05
SMART CLASSROOM

## Slide 6
LIVE DASHBOARD
Real-time monitoring for instructors
06
SMART CLASSROOM

## Slide 7
HARDWARE INTEGRATION
ESP32-driven physical alerts
Components
• ESP32 DevKit V1
• 3x status LED (green / yellow / red)
• Active piezo buzzer
• 16x2 I2C LCD
• Reserved GPIO for future servo
JSON Command Protocol
{
"cmd": "alert",
"severity": "critical",
"led": "red",
"buzzer_ms": 800,
"lcd_line1": "ALERT",
"lcd_line2": "Low Attention"
}
POST over WiFi to the ESP32's local HTTP server — fails gracefully (logged, non-fatal) if hardware is offline.
07
SMART CLASSROOM

## Slide 8
VALIDATION
Clear separation between attention states
Chart: Attention Engine Output on Test Signal Profiles
| Fully Attentive | Distracted | Drowsy / Yawning
Attention Score | 92.4 | 58 | 27
Automated Test Suite
21 / 21
assertions passing
3
modules under test
0
known open bugs
08
SMART CLASSROOM

## Slide 9
FUTURE SCOPE
Where this goes next
Edge Deployment
Quantized on-device models for classroom-local hardware without a GPU server.
Servo-Actuated Camera
Multi-angle coverage — firmware protocol already reserves a servo command slot.
Semester-Long Trends
Longitudinal engagement modelling correlated with assessment outcomes.
Stronger Privacy
Federated or on-device face-encoding storage beyond server-side Firestore.
09
SMART CLASSROOM

## Slide 10
Thank You
Smart Classroom — AI-Powered Engagement & Attention Tracking System
Questions & Discussion